## Slide 1
EXECUTIVE SUMMARY • HACKATHON FINAL
SleepLens: Dual-Tier AI for Sleep Stage Classification & Sleep Quality Assessment
Bridging 30-Second Discrete Staging with Continuous Depth Dynamics & Microstructural Phenotyping
⚠️ The Clinical Bottleneck
• Standard overnight PSG requires 1.5–2 hours of manual visual scoring per recording.
• Inter-scorer agreement is notoriously low on transitions (N1 < 60%).
• Coarse 5-stage AASM scoring discards continuous sleep depth and cortical synchronization dynamics.
🧠 Dual-Tier AI Engine
• Tier 1 (Staging): 4-Model Ensemble Macro-F1 0.8425 (Cohen's κ 0.831) across 237,936 epochs.
• Tier 2 (Depth): SDI Transformer (npj Digital Med 2025) continuous 0–1 depth trajectory + 96 clinical parameters.
• Minimal Sensors: 2-sensor montage (Fpz+EOG) retains 99.5% F1 performance!
💻 Production Platform
• Full-stack clinical webapp: Next.js 14 + Django REST Framework.
• Interactive hypnograms, continuous depth curves, and raw microvolt signals explorer.
• Automated LLM clinical report + OpenCode interactive diagnostic assistant.
SleepLens Platform • Confidential & Clinical Research Prototype
Slide 1 of 9 • 0:00–0:45
Notes: Target: 0:00 - 0:45 (45s)
Good morning. Today we present SleepLens, an end-to-end clinical AI platform designed to transform sleep diagnostics. Polysomnography is gold standard, yet analyzing 8 hours of multichannel PSG takes hours of tedious manual scoring and collapses complex neurobiology into 5 discrete stages. SleepLens solves this with a two-tiered AI system: an ensemble staging model with calibrated uncertainty, and a continuous sleep depth transformer with a 96-feature phenotyping engine, deployed in a production-ready clinical web application.

## Slide 2
BENCHMARK & EXPERIMENTAL INTEGRITY
Dataset, Preprocessing & Standardization
Sleep-EDF Expanded: Full 197 nights with leakage-free subject-atomic cross-validation
0:45 – 1:30 | 45s
📊 Full Benchmark: Sleep-EDF Expanded (PhysioNet)
Scale & Volume:
• 197 all-night recordings (~2,000 hours of continuous PSG) • 237,936 validated 30-second epochs (epochs_v3 benchmark)
Dual-Cohort Validation (Never Confounded):
• Sleep Cassette (SC): 153 recordings (ambulatory healthy subjects) • Sleep Telemetry (ST): 44 recordings (in-patient clinical cohort)
Leakage-Free Protocol: Subject-Atomic 5-Fold CV
• Zero subject overlap between training, tuning, and testing (folds5_v3) • Prevents overoptimistic memorization seen in subject-leaked studies.
⚙️ Signal Harmonization & Preprocessing
1. Canonical 100 Hz Resampling
Polyphase anti-aliasing filtering across all raw input channels to eliminate sample rate divergence across hospital equipment.
2. Electrode Standardization
Harmonizes diverse montages to canonical channels: Frontal EEG (Fpz-Cz), Occipital EEG (Pz-Oz), Ocular (EOG horiz), Chin (EMG submental).
3. Lights-Off Windowing (BENCHMARK_30)
Automatically cuts extensive pre/post recording waking padding while strictly preserving sleep onset and offset transition dynamics.
Evaluation Protocol: Subject-disjoint 5-fold cross validation with unified benchmark windowing
BENCHMARK_30 Window: 237,936 valid epochs
Notes: Target: 0:45 - 1:30 (45s)
To ensure clinical validity, we used the full Sleep-EDF Expanded dataset across all 197 nights and nearly 238,000 epochs. Unlike many published papers that suffer from subject leakage, we enforced a strict subject-atomic 5-fold cross-validation scheme. We evaluated both cohorts: ambulatory cassette and clinical telemetry. Every recording is harmonized to 100 Hz, with standardized electrode alignments and automated lights-off windowing to ensure fair, reproducible benchmarking.

## Slide 3
TIER 1 AI MODEL
30-Second Sleep Stage Classification (SSC)
Systematic benchmark of 25+ configurations across all 197 nights
1:30 – 2:25 | 55s
Run | Architecture / Montage | Macro-F1 | SC F1 | ST F1 | N1 F1 | N2 F1 | N3 F1 | REM F1 | Cohen κ
E19 (Best) | 4-Model Diverse Ensemble (ANY3ch + ANY2ch + USleep + LGBM) | 0.8425 | 0.836 | 0.865 | 0.635 | 0.892 | 0.833 | 0.915 | 0.831
E11 | AnySleep 3ch (Fpz+Pz+EOG) — Best Single Model | 0.8267 | 0.809 | 0.878 | 0.622 | 0.880 | 0.788 | 0.904 | 0.812
E11d | AnySleep 2-Sensor (Fpz+EOG) — Best 2-Sensor | 0.8227 | 0.811 | 0.865 | 0.592 | 0.880 | 0.812 | 0.905 | 0.808
E20 | RobustSleepNet Fpz (Clean Baseline — No Sleep-EDF) | 0.7501 | 0.736 | 0.788 | 0.442 | 0.828 | 0.717 | 0.855 | 0.724
E00 | LightGBM (11 Spectral/Bandpower Features) | 0.6672 | — | — | 0.339 | 0.752 | 0.687 | 0.585 | 0.612
E01 | YASA Clinical Baseline (Fpz-Cz Random Forest) | 0.5225 | 0.486 | 0.611 | 0.100 | 0.737 | 0.538 | 0.557 | 0.473
1. Diversity Beats Scale
Adding our weak LightGBM model (0.667 F1) boosted deep models by +0.016 F1 because it captures orthogonal spectral features rather than raw waveforms.
2. Record Class Breakdown
Winning ensemble sets benchmark records across all 4 key sleep stages: N1 (0.635), N2 (0.892), N3 (0.833), and REM (0.915).
3. Viterbi Rejected
Viterbi transition prior degraded performance (0.8267 → 0.8259) because AnySleep already has an intrinsic 14-minute temporal receptive field.
Winning 4-member ensemble: Fold-honest OOF evaluation agreement across all 5 folds
Cohen's κ = 0.831 (Matches expert human consensus)
Notes: Target: 1:30 - 2:25 (55s)
For sleep stage classification, we systematically benchmarked 25+ configurations. Classical heuristics like YASA struggle severely on N1 sleep at only 0.10 F1. Deep neural models like AnySleep perform exceptionally at 0.8267. Our winning system, E19, is a 4-member fold-honest ensemble combining AnySleep 3-channel, AnySleep 2-channel, U-Sleep CSDP, and our engineered LightGBM model. It reached 0.8425 Macro-F1 with a Cohen's Kappa of 0.831. Crucially, the weak LightGBM model improved the ensemble by introducing non-redundant spectral feature diversity.

## Slide 4
SSC ENGINEERING INSIGHTS
Sensor Ablation & Explainable AI (XAI)
Finding the minimal wearable configuration and auditing deep network attention
2:25 – 3:15 | 50s
🔌 Channel Ablation: Minimal Hardware Montage
Full 3-Channel (Fpz-Cz + Pz-Oz + EOG) ──▶ 0.8267 F1 (Ref)
★ 2-Sensor Setup (Fpz-Cz + EOG) ──▶ 0.8227 F1 (-0.004 Δ)
Dual EEG (Fpz-Cz + Pz-Oz, no EOG) ──▶ 0.8134 F1 (-0.013 Δ)
Single Frontal EEG (Fpz-Cz Only) ──▶ 0.8015 F1 (-0.025 Δ)
Single Occipital EEG (Pz-Oz Only) ──▶ 0.7736 F1 (-0.053 Δ)
Clinical Finding: Posterior EEG (Pz-Oz) is droppable. Adding EOG to frontal EEG captures ocular dipole saccades directly, boosting true REM recall to 0.913 (vs 0.897 on full 3-channel).
🔍 Attention Routing & Uncertainty Calibration
Layer 12 Skip-Connection Channel Attention Routing:
• WAKE: 67.2% Pz Attention (Occipital alpha rhythm tracking)
• N3 DEEP: 93.0% EEG Attention (Slow-wave cortical sync, eyes quiet <7.1%)
• REM SLEEP: 52.0% EOG Attention (Saccadic burst tracking during atonia)
Monotonic Confidence Calibration (ECE = 0.029):
• Conf ≥ 0.90 (30.3% of night): 99.5% empirical accuracy. • Conf < 0.60 (~15% of night): Flagged with needs_review = true. • Doctor-in-the-Loop: Clinicians inspect only uncertain epochs.
Hardware Target: 2-Sensor Wearable Headband (Fpz-Cz + EOG)
Expected Calibration Error (ECE) = 0.029
Notes: Target: 2:25 - 3:15 (50s)
Two practical questions: Can we run this on a minimal home device, and is the model interpretable? Our ablation proved that a two-sensor setup—one frontal EEG and one EOG—achieves 0.8227 F1, losing only 0.004 compared to three channels while actually improving REM detection. Deep skip-layer attention reveals the network dynamically shifts attention to posterior alpha in Wake, slow waves in N3, and surges to 52% EOG attention during REM. Finally, our confidence calibration is monotonic: epochs above 90% confidence are 99.5% accurate, enabling intelligent human-in-the-loop triage.

## Slide 5
TIER 2 AI MODEL
Continuous Sleep Depth (SDI) & 96-Feature Engine
Transcending 5 discrete steps into continuous neurobiological synchronization
3:15 – 4:05 | 50s
SDI Transformer Network (Zhou et al., npj Digital Medicine 2025)
Computes a continuous Sleep Depth Index (0.0 = Light/Wake to 1.0 = Deep SWA Sink) per 30-s epoch. Unlike discrete AASM staging, SDI quantifies gradual micro-arousals, sleep debt dissipation, and cyclic alternating patterns (CAP).
Standardized Research Vector: [RB: SDI < 0.20 Shallow Burden] • [AP: Mean Sleep Depth] • [CV: Instability SD/Mean] • [MDR: Mean REM Depth] • [PR: Model REM Share]
📈 96-Parameter Physiological Extraction Engine
Continuity & Fragmentation
• Total Sleep Time, TIB, SE% • SOL, WASO, REM Latency • Awakening Index • Sleep Fragmentation Index
Architecture & Dynamics
• % N1, N2, N3, REM of TST • 1st vs 2nd half stage shifts • Bout duration statistics • 5x5 Markov Transition Matrix
Spectral Power Dynamics
• Welch Powers (δ, θ, α, σ, β) • Slow Wave Activity (SWA) • Spectral Entropy • Permutation Entropy
Microstructure & Muscle
• YASA Spindle Density (N2) • Slow Wave Amplitude & Dur • Submental EMG RMS • REM Muscle Atonia Ratio
Dual Perspective: Discrete 30s macro hypnogram + Continuous microstructural depth
Output: 96 clinical parameters per night
Notes: Target: 3:15 - 4:05 (50s)
In Tier 2, we transcend discrete 5-stage hypnograms. We implement the Sleep Depth Index Transformer from Zhou et al., published in npj Digital Medicine 2025. This computes a continuous 0.0 to 1.0 sleep depth score for every epoch, capturing micro-arousals and depth dynamics that discrete staging obscures. In tandem, our feature extraction engine computes ~96 clinical parameters per night: sleep continuity, 5x5 Markov transition matrices, spectral bandpowers, and microstructural events like YASA sleep spindle density and REM muscle atonia ratios.

## Slide 6
CLINICAL INTELLIGENCE
Sleep Quality Index & Multi-Modal Scoring
Synthesizing 96 physiological parameters, continuous depth, and patient perception
4:05 – 4:55 | 50s
🎯 SleepLens Unified Sleep Score (0–100)
A transparent, non-black-box 100-point composite formula:
• Sleep Efficiency (SE%): Max 25 pts (TST / Time in Bed)
• Continuous Sleep Depth: Max 25 pts (Mean SDI slow-wave saturation)
• Sleep Continuity: Max 20 pts (Shift index & awakenings penalty)
• Deep Sleep Share (N3%): Max 10 pts (Physical restoration)
• REM Sleep Share (REM%): Max 10 pts (Cognitive restoration)
• Sleep Onset Latency (SOL): Max 5 pts (<30 min target)
• Fragmentation Resistance: Max 5 pts (Shallow SDI <0.20 burden)
Clinical Grading: ≥85: Excellent | 70–84: Good | 55–69: Fair | <55: Poor
🩺 Subjective-Objective Synthesis (PSQI)
Standardized PSQI Integration (0–21 Global):
Includes all 7 clinical component domains (latency, duration, efficiency, disturbances, meds, daytime dysfunction). Directly compares patient perception against objective EEG signals.
Sleep State Misperception Detection:
Identifies paradoxical insomnia: high subjective distress (PSQI > 12) despite objectively normal sleep architecture (SE > 85%, deep N3 intact).
Automated Clinical Narrative Synthesis:
LLM generator (gpt-6-luna) formats 96 metrics, continuous depth, and PSQI into structured clinical findings ready for physician sign-off.
Clinical Utility: Converts 96 engineering parameters into intuitive patient scoring
Transparent, non-black-box composition
Notes: Target: 4:05 - 4:55 (50s)
To synthesize these complex metrics into an actionable patient indicator, we designed the SleepLens Unified Sleep Score. Rather than an uninterpretable black-box score, it is a transparent 100-point scale: 25% sleep efficiency, 25% continuous depth, 20% continuity, and the remainder distributed across N3 deep sleep, REM, latency, and fragmentation. We also incorporate the standardized 7-component PSQI questionnaire. By contrasting subjective perception against objective PSG signals, SleepLens can flag paradoxical insomnia and feeds all metrics into an automated clinical reporting engine.

## Slide 7
SYSTEM DESIGN
End-to-End System Architecture & Data Flow
Scalable decoupled asynchronous processing pipeline from raw EDF to diagnostic report
4:55 – 5:45 | 50s
01 • UPLOAD & AUTH
• Drag & drop EDF (≤500 MB) • Optional 7-part PSQI form • Patient metadata linkage • JWT httpOnly security
02 • SIGNAL PIPELINE
• Canonical 100 Hz resample • Lights-off windowing • Channel QC & alignment • Celery async worker queue
03 • DUAL AI ENGINES
• Tier 1: 4-Model Ensemble (Staging + Confidence) • Tier 2: SDI Transformer (Continuous depth 0–1)
04 • CLINICAL PLATFORM
• SleepLens Score (0–100) • 96-parameter engine • Automated LLM report • OpenCode consultation chat
Production Technology Stack & Data Contracts (Fully Containerized)
• Frontend UI: Next.js 14 App Router, TypeScript, Tailwind CSS, Zustand, React Query. • Backend Core: Django REST Framework, PostgreSQL, Celery asynchronous workers, Redis broker. • Machine Learning: PyTorch, MNE-Python, LightGBM, YASA, SciPy signal processing. • Intelligence Layer: OpenAI API (gpt-6-luna) for diagnostic narrative; OpenCode local agent for consultation.
Decoupled architecture: ML workers never block web tier API requests
Average end-to-end processing: < 35 seconds on 8-core CPU
Notes: Target: 4:55 - 5:45 (50s)
Here is our production system architecture. A clinician uploads an EDF file and optional PSQI through the Next.js web application. The Django REST backend sanitizes the upload and delegates heavy computation to Celery workers backed by Redis. Signals are canonically harmonized to 100 Hz, passed in parallel through both AI tiers—the 4-model staging ensemble and the SDI transformer—and combined with the 96-feature engine. Results are indexed in PostgreSQL and rendered back to the clinician with an LLM clinical report and an OpenCode consultation assistant.

## Slide 8
THE PRODUCT
Clinical Web Application (SleepLens UI/UX)
Comprehensive diagnostic cockpit built specifically for sleep physicians and technologists
5:45 – 6:30 | 45s
🎯 SleepLens ScoreCard & Core KPIs
• Unified Score Gauge (0–100) with 7-part breakdown. • Core KPIs: Total Sleep Time (412.5 min), Sleep Efficiency (88.4%), SOL (14.0 min), WASO (38.5 min), REM Latency (78.0 min), Staging Confidence (91.2%).
📊 Interactive Hypnogram & Confidence Bands
• Synchronized 30-s stage timeline (Wake, REM, N1, N2, N3). • Confidence overlay: High (≥80%), Medium (≥60%), Low (<60%). • One-click review flags for borderline epochs requiring human check.
📈 SDI Sleep Depth Curve & Raw Signal Explorer
• Continuous 0.0–1.0 Depth Waveform: Highlights cortical synchronization dips. • Signals Explorer: Zero-latency raw microvolt inspection for any 30-second epoch (Fpz-Cz, Pz-Oz, EOG, EMG).
💬 Automated AI Report & Consultation Assistant
• Clinical Narrative: LLM-generated report formatted in Markdown with clinician sign-off. • OpenCode Assistant: In-session interactive chat answering study-specific questions grounded in patient data.
Responsive Next.js Frontend • Modern Slate & Teal Medical Theme
Reduces clinician visual scoring time by >85%
Notes: Target: 5:45 - 6:30 (45s)
This slide showcases the clinician interface. The dashboard presents the SleepLens Score and core KPIs at a glance. Below, the interactive hypnogram is coupled with real-time confidence tracking, highlighting exactly which epochs need human verification. Clinicians can view continuous sleep depth, open the raw signal viewer to inspect EEG microvolts for any 30-second epoch, review the AI-drafted diagnostic report, or ask questions in the OpenCode consultation chat. It reduces scoring overhead from 90 minutes down to a quick verification.

## Slide 9
CONCLUSION & IMPACT
Deployment Performance & Future Roadmap
Real-world speed benchmarks, clinical impact, and wearable translation
6:30 – 7:00 | 30s
⚡ CPU Speed Benchmarks (8-Core CPU, No GPU)
• Single Epoch Inference: 3.7–4.7 ms (×6,400 real-time)
• Full 22-Hour Night PSG (2,650 ep): 12.5 seconds (Ensemble)
• Continuous SDI Depth Inference: 8.2 seconds (Transformer)
• 96-Parameter Extraction: 9.8 seconds (Welch+YASA)
★ Total Pipeline Turnaround: < 35 seconds per night!
Clinical Productivity Impact: Reduces manual physician visual scoring time by >85% while delivering far deeper physiological insights and automated audit trails.
🚀 Translational Roadmap
1. Wearable Surrogate Translation
Deploying our trained ResUNet and WatchSleepNet surrogate models for wrist-worn actigraphy and PPG without any EEG leads.
2. Formal Apnea & Movement Scoring
Upgrading our proxy detectors to formal clinical AASM Apnea-Hypopnea Index (AHI) and Periodic Limb Movement Disorder (PLMD) scoring.
3. Multi-Center Clinical Trials
Validation across large sleep cohorts (Sleep Heart Health Study) and neurological disorder groups (Parkinsonian REM sleep behavior disorder).
SleepLens: Delivering Clinical Precision with Real-Time Efficiency
Thank you! Questions & Discussion
Notes: Target: 6:30 - 7:00 (30s)
In summary, SleepLens delivers state-of-the-art staging accuracy of 0.8425 F1 and 0.831 Kappa, with a complete turnaround time under 35 seconds on standard CPU hardware. By uniting discrete stage classification, continuous depth modeling, and automated clinical reporting, we cut physician scoring time by over 85% while providing unprecedented diagnostic depth. Our minimal two-sensor finding also enables accurate home wearable monitoring. SleepLens bridges machine learning with the daily realities of clinical sleep medicine. Thank you.